|  | The Hong Kong University of Science and Technology Health, Safety and Environment Office 香港科技大學 健康、安全及環境處 |
| --- | --- |

Entry Procedures for Main Building Service Tunnel

進入大樓維修隧道的程序

- Health, Safety and Environment Office should be informed before the entry when hazardous operations (such as welding and use of chemicals, etc.) have to be done inside the Service Tunnel.

若要在維修隧道內進行具有任何危險性工作 (例如燒焊及使用化學物品等等)，必須事先通知健康，安全及環境處。

- Before entering the Service Tunnel, the entrant must notify BS Duty Controller at LG7 BS Workshop and record the details of entry into the “Service Tunnel In/Out Record Book” which is kept in the control room.

進入維修隧道前，進入者必需通知地下七樓 (LG7) BS工場內的當值控制員和登記有關的資料於控制室內的『維修隧道進入/離開記錄冊』 。

- The entrant must wear a safety helmet, bring along a walkie talkie and a torch.

進入維修隧道者應佩戴安全頭盔，攜帶對講機和電筒。

- The entrant must inform BS Duty Controller to turn on the ventilation system and lighting of the Service Tunnel 30 minutes in advance. He should also familiarize with different exits by studying the affixed location layout in the Service Tunnel before the entry. Leave the Tunnel immediately if the ventilation fan(s) is/are not functioning properly, and inform BS Duty Controller.

進入維修隧道者必須知會BS當值控制員，預先30分鐘前開啟維修隧道內的抽風系統，正常燈光，還有參考附貼在維修隧道內的位置圖以熟認不同的出口。若隧道內之抽氣扇不能正常操作，應立即離開隧道和通知BS當值控制員。

- In case of accident or feeling uncomfortable, the entrant(s) must evacuate from the Service Tunnel at once. Seek help from Security Control Centre and inform BS Duty Controller immediately.

進入者如遇意外或感覺不舒適，應立刻離開維修隧道。立刻向保安控制中心尋求援助和通知BS當值控制員。

- Solo operation in the Service Tunnel should be avoided. If this cannot be practicably avoided, the entrant should maintain frequent contact with BS Duty Controller (at least every 30-minute).

應避免在維修隧道內單獨逗留或工作。若不能避免，進入者必須與BS當值控制員保持緊密聯絡﹝最少每隔30分鐘聯絡一次﹞。

- For inquiry, please contact BS Duty Controller at ext. 6465.

若有任何疑問，請聯絡 BS當值控制員，內線 6465查詢。